Matlab Server

login in to maltab server
   1) open terminal
   2) type: mats

logout
   type twice: exit

open matlab on server
   type: mat
   or : matno #(for no display)

How to copy from ganges to server-ganges
cd ~/ganges/
sh pullFromGanges data/(dir you want to copy)/
otherwise use scp

Chipod / GusT Processing

1 Preparation (80% of labor work)
1. create folder tree
2. collect available mooring data
3. create vel_m.mat
4. create dTdz_m.mat
5. create header.mat
6. create header_p.mat (Pitot calibration) (!!!! main step !!!)

1.1 create folder tree
This step is only necessary if Pavan hasn't yet generated the right folder tree. For all new Chipods
Pavan will do this already on ganges.
If folder tree not ready yet:
- go to 'cd /ganges/work/template/chipodGustFolderTree/'
- copy 'unit' directory to deployment directory and rename it with unit name (for instance 524)
- there should be a couple of sub folders, one is called './raw' : copy all raw files of your chipod to this directory (alternatively if using mac or linux you could link to the raw files by using 'ln -sf source target')

1.2 collect all available mooring data
Find all relevant mooring data like salinity, temperature, and velocity close by.

1.3 create vel_m.mat
If you have velocity data available you should interpolate them on the chipod depth and save in the following format
vel_m.time	(matlab time),
vel_m.u	(east velocity),
vel_m.v	(north velocity),
vel_m.spd	(speed)

and save('../input/vel_m.mat', 'vel_m');

If you want you could also use the routine chi_pre_driver.m . To this end set the flag
 do_vel_m = 1; in chi_pre_driver.m and provide path to your velocity input file in the corresponding section.
If you want to use an mooring file that was used for old processing the code block in chi_pre_driver.m would look like:
if do_vel_m
    sdir = [basedir filesep 'input' filesep];
    load('../../../mooring_data/mooring_Pirata14_524.mat') ;
    chi_generate_vel_adcp(moor.time, moor.depth, moor.u, moor.v,...	moor.depth, sdir)
end

1.4 create dTdz_m.mat
The aim is to create a file called dTdz_m.mat in the input directory. This file should contain a structure called Tz_m with the following fields:
Tz_m.time	(matlab time)
Tz_m.Tz	(vertical temperature gradient)
Tz_m.N2	(vertical stratification)

You can either create this file directly or you use chi_pre_driver.m in the mfile directory of your unit directory. In this file set do_dTdz_m = 1; and change the corresponding section, providing your
mooring data as input.

If you want to use an old mooring file you simply load this file and than say
Tz_m.time	= moor.time;
Tz_m.Tz	= moor.dTdz;
Tz_m.N2	= moor.N2;
 save('../input/dTdz_m.mat', 'Tz_m');

1.5 create header.mat
There need to be a header.mat in /unit/calib/ . Normally Pavan puts it there already. If it is not there
the software should realize it is missing and will ask you if it should generate such file from the raw-file. To this end:
- run test_individual_raw_files.m with all flags set to 0
- a dialog window should pop up if you want to generate header.mat from raw file
- once the routine finished type in the command window:
  - save('../calib/header.mat', 'head')
- maybe you run into the problem that ./calib/header_p.mat is missing while running test_individual_raw_files.m, (solution see next subsection)

1.6 create header_p.mat (Pitot calibration)
There need to be a header_p.mat in /unit/calib/ . Normally Pavan puts it there already. If not you have to follow the following steps (or ask Pavan)
- load ../calib/header.mat
- type in the command window head.sensor_id
- this should give you a list of sensor IDs (for instance 14-44 )
- go to the base calibration folder ../Calibrations/Pitot_Cals/ There should be a number of png files, choose the one that belongs to your sensor id (if you cannot find them: ask Pavan or Byungho for calibration coeffs (all these should be saved at a central point on ganges))
- you need a structure called W containing W.Ps , W.T, W.Pd, W.Tilt. (These fields contain the calibration of the Pitot tube: Ps: pressure, T : temperature, Pd: dynamic pressure, Tilt: tilt)
- each of these should be a 5 element vector where only the second element is relevant. Put the slopes from the figure into the second element of the vector like
1. W.T	= [0 slope_value(3rd pannel) 0 0 0];
2. W.Ps	= [0 slope(4th panel) 0 0 0];
3. W.Tilt	= [0 slope(2nd panel) 0 0 0];
4. W.Pd	= [0 1/slope(1st panel) 0 0 0]; (%if slope>1 else W.Pd = [0 slope 0 0 0];)
The W structure should be saved in ../calib/header_p.mat

Hint: For older chipods you might want to consider putting W.Ps(2) = 0; to switch off common mode pressure calibration, because the pressure sensor drifts away over longer periods, which would corrupt the Pitot calibration.

The above four fields contain the necessary slopes for the Pitot calibration, however you must add the off sets (W.V0, W.P0 and W.T0) by following one of the following procedure.

Tune V0 to available data (if you generated a vel_m.mat in step 1.3)
Use test_individual_raw_files.m
(1) set the flags as follows:
%_____________________flags______________________
do_adcp = 1; % do you have ADCP data to compare with
header_offset = 0; % use offset data from pitot header
get_v0_hist = 0; % detremine v0 from histogram
get_v0_fit = 1; % detremine v0 from adcp fit
do_vel_plot = 1; % make a big velocity comparision figure
do_eps = 0; % calculate disspation rates from Pitot

(2) then go to the line that follows
      % maual pick off sets
        data.cal.V0 = 0;
        data.cal.T0 = 20;
        data.cal.P0 = 0;
choose V0 = 0 to begin with, T0 should be an average values that fits your entire data set. Does not need to be very accurate, but it should be kept constant for the later analysis. P0 cschould represent the
depth of the chipod in [psi]. (if you switched off pressure calibration [see above] you can choose any value here).
(3) set the file id to any value (the number determines which raw_file will be used)
ifid = 2;
(4) run test_individual_raw_files and note the result for V0_adcp

Find V0 wvia histogram
Use test_individual_raw_files.m
(1) set the flags as follows:
%_____________________flags______________________
do_adcp = 0; % do you have ADCP data to compare with
header_offset = 0; % use offset data from pitot header
get_v0_hist = 1; % detremine v0 from histogram
get_v0_fit = 0; % detremine v0 from adcp fit
do_vel_plot = 0; % make a big velocity comparision figure
do_eps = 0; % calculate disspation rates from Pitot

(2) then go to the line that follows
      % maual pick off sets
        data.cal.V0 = 0;
        data.cal.T0 = 20;
        data.cal.P0 = 0;
choose V0 = 0 to begin with, T0 should be an average values that fits your entire data set. Does not need to be very accurate, but it should be kept constant for the later analysis. P0 cschould represent the
depth of the chipod in [psi]. (if you switched off pressure calibration [see above] you can choose any value here).

(3) set the file id to any value (the number determines which raw_file will be used)
ifid = 2;
(4) run test_individual_raw_files and note the result for V0_hist
(5) repeat (3) and (4) with a different file, you should try at least 3 to 10 files and see
if the values of V0 stay constant, if thats the case you can proceed to (6)
(6) If you decided on a set of T0 P0 and V0 you should add them to the W structure
W.T0 = T0; W.P0 = P0; W.V0 = V0;
and then save W in ../calib/header_p.mat
done

A general rule is: It is better to under than to over estimate V0.

2. Pre-processing (10 %)
1. process temp.mat
2. process pitot.mat
3. process dTdz_i.mat
2.1 process temp.mat
You can process the entire chipod data set for non turbulence data to obtain a high resolution
temp structure in ./proc/temp.mat. To this end use again chi_pre_process.m with the flags
%_____________________set processing flags______________________
   do_parallel = 1; % use paralelle computing
   do_temp = 1; % generate temp.mat
   do_vel_p = 0; % generate vel_p.mat
   do_vel_m = 0; % generate vel_m.mat
   do_dTdz_m = 0; % generate dTdz_m.mat
   do_dTdz_i = 0; % generate dTdz_i.mat
At the beginning you might want to switch do_parallel =0; to see if you run into any errors. If the first
couple of files are processed successfully you can stop the processing and switch back to
do_parrallel = 1;
By default the matlab cluster will use 16 processors. Like this one chipod year should take approximately 1h to process for temp.mat.

2.2 process pitot.mat
You can process the entire chipod data set for the pitot velocity to obtain a high resolution
velocity structure in ./proc/pitot.mat. To this end use again chi_pre_process.m with the flags
%_____________________set processing flags______________________
   do_parallel = 1; % use paralelle computing
   do_temp = 0; % generate temp.mat
   do_vel_p = 1; % generate vel_p.mat
   do_vel_m = 0; % generate vel_m.mat
   do_dTdz_m = 0; % generate dTdz_m.mat
   do_dTdz_i = 0; % generate dTdz_i.mat
At the beginning you might want to switch do_parallel =0; to see if you run into any errors. If the first
couple of files are processed successfully you can stop the processing and switch back to
do_parrallel = 1;
By default the matlab cluster will use 12 processors. Like this one chipod year should take approximately 1h to process for pitot.mat.

Once you have your pitot.mat, you could run compare_velm_to_pitot.m, which will generate
a comparison between the Pitot tube and mooring velocity data. This could be useful to check if the choise of V0 was good or if there are any compass problems in the chipod.

2.2 process dTdz_i.mat
Finally, you might want to calculate the stratification internally from the chipod. Note! This should
only be done for surface wave pumped chipods. The processing will generate a new input file in the input folder called dTdz_i.mat
You can process the entire chipod data set for the dTdz_i. To this end use again chi_pre_process.m with the flags
%_____________________set processing flags______________________
   do_parallel = 1; % use paralelle computing
   do_temp = 0; % generate temp.mat
   do_vel_p = 0; % generate vel_p.mat
   do_vel_m = 0; % generate vel_m.mat
   do_dTdz_m = 0; % generate dTdz_m.mat
   do_dTdz_i = 1; % generate dTdz_i.mat
At the beginning you might want to switch do_parallel =0; to see if you run into any errors. If the first
couple of files are processed successfully you can stop the processing and switch back to
do_parrallel = 1;
By default the matlab cluster will use 12 processors. Like this one chipod year should take approximately 40min to process for dTdz_i.mat.

If you want to add additional Salinity information you could use a function that translate a given T-S relation and Tz into N2. Ask Johannes for more information. If you believe that salinity is not important for N2 you can skip this step.

3. Main processing (10 %)
Do main processing using

Processing flags
epsp	:	pitot epsilon processing

INPUT	vel_m (ADCP)	Pitot
dTdz_m (chipod)	mm1, mm2	pm1, pm2
dTdz_i (chipod)	mi1, mi2, mi12	pi1, pi2, pi12
dTdz_m (gusT)	mmg	pmg
dTdz_i (gusT)	mig	pig